## Slide 1: RoboCup Junior Victoria
Programming Spike Prime
Using MicroPython

## Slide 2: Robot programming
What are the programming challenges and how are they best approached?

## Slide 3: Rescue Robot Programming
Rule #1 – Construction impacts programming
Rule #2 – Programming impacts construction
Simplicity is the key to successful programming, especially for beginners. If it looks more complicated than necessary, it probably is.

## Slide 4: Introduction to the coding interface Opening a new project
From the HOME page
Tutorials
Teaching unit plans
Build instructions
Links to your recent projects
New Project
Open a new coding window
Choose to code in either
  WORD BLOCKS (Scratch)
  PYTHON
This presentation will focus on coding with Python

## Slide 5: Introduction to the “Application Programming Interface” (API)
Quick view of port connections
For details click on the brick icon to open the “Dashboard”
How it looks to you will depend on the ports that you are using
Default code included automatically
Lines 1-3 are Python code libraries that you are likely to use
Line 5 initialises the PrimeHub() class as hub
Line 7 will display a “happy face” on the hub

## Slide 6: Dashboard
DASHBOARD (if connected)
Battery level indicator
Port position for all connected inputs and outputs
  All ports can act as either input or output ports
Readings from each port
  What is viewed can be set using the dropdown menu
MANAGE PROGRAMS
Hub can hold up to 20 programs
Options for deleting programs held on hub

## Slide 7: Support – Built in ‘Knowledge Base”
The Knowledge Base
Hidden on the right side of the screen
“Getting Started” contains a limited introduction to programming in Python
  Specifically tied to Spike Prime inputs and outputs
  Provides examples and challenges
  Helps to be familiar with Python
More details are provided in additional dropdowns listed below “Getting Started”

## Slide 8: Example of simple program
Things to note:
Encourage students to add comments to explain code (the comments are a bit overdone in this example)
When ready to download code to robot, click on the 5 x 5 grid at the bottom to select the program storage position (0 – 19) on the hub
Click on the down arrow to download to hub

## Slide 9: Identifying errors and getting help
If you run the program while connected to the computer, error information will show up in the Console
In this example, the units used in the code are not acceptable
The Knowledge Base will provide details of necessary and acceptable parameters
Note: “Short range” is from 5-30 cm. Default is from 5-200 cm.

## Slide 10: Line following
What are the programming challenges and how are they best approached?

## Slide 11: Rescue Robot Programming
Where to start?
All Rescue divisions require the robot to:
Follow a line
Locate victim
One light sensor or two?
Riley Rover Rescue (Victoria only) only needs one
All other divisions require two

## Slide 12: Principles of Line Following
Case 2
While True: # robot on
  While sensor sees white:
    Turn right
  While sensor sees black:
    Turn left
Case 1
While True: # infinite loop
  If sensor sees white:
    turn right
  If sensor sees NOT white:
    turn left
What does this look like in code?
Please note: I have not included comments with all example codes. A good exercise for the students is for them to add comments. It forces them to think through the code and also helps them to see the important role that comments play.

## Slide 13: Single Sensor – Case 1
Case 1
While True: # infinite loop
  If sensor sees white:
    Turn right
  Else:
    Turn left

## Slide 14: Single Sensor – Case 2
Case 2
While True: # infinite loop
  Turn right
  Until sensor sees black
  Turn left
  Until sensor sees white

## Slide 15: Single Sensor
I have used colour detection (black-white)
Could this be done using reflected light instead?
How do you decide what to set the reflected light intensity to?
Why would you choose one over the other?
Do motor speed settings matter?
Common pitfalls
Movement motor ports not set
Sensor/motor ports in program don’t correspond to ports used on robot
Motors mounted in reverse orientation
Code needs to be optimised for the robot build and light conditions

## Slide 16: Adding a second sensor
Case 2
While True: #robot on
  If sensor_left sees white AND sensor_right sees white:
    go straight
  If sensor_left sees white AND sensor_right sees black:
    turn right
  If sensor_left sees black AND sensor_right sees white:
    turn left
  If sensor_left sees black AND sensor_right sees black:
    # Will this ever occur??? What should happen???
Case 1
While True: # robot on
  While sensor_left sees black:
    Turn left
  While sensor_right sees black:
    Turn right
What does this look like in code?

## Slide 17: Double sensor – Case 1
Consider colour vs reflected light, reflected light cut-off values, motor speed settings
Case 1
While True: # infinite loop
  Turn right
  Until sensor_left sees black
  Turn left
  Until sensor_right sees black
The “less_than” operator function needs to be imported from the spike library. This is not one of the default imports.

## Slide 18: Double sensor – Case 2
What does the “else” condition represent?
Will your robot ever encounter this?
Could this be used to detect green?

## Slide 19: Proportional line follower
What if I could adjust the amount the robot turns by how far off the line it is?
Would this make for a much smoother run along the line?
No correction required
Large correction required
While True: #robot on
  Input sensor_left value
  Input sensor_right value
  Turn_value = (sensor_left – sensor_right)  correction_factor
  Input turn_value to Move Steering block # if sensor_left > sensor_right, turn_value > 0 and robot turns right
  # if sensor_left < sensor_right, turn_value < 0 and robot turns left

## Slide 20: Proportional line follower
3
2
3
No correction
Both sensors on white
98 – 98 = 0
steering = 0
Robot goes straight
Small correction
Right sensor on edge (86)
Left sensor on white (98)
86 – 98 = -12
steering = -12  2.0 = -24
Robot turns slight right
Large correction
Right sensor on white (98)
Left sensor on black (28)
98 – 28 = 70
steering = 70  2.0 = 140 (NB: max is 100)
Robot turns hard left
No correction required
Larger correction required
Small correction required

## Slide 21: Rescuing the victim
What are the programming challenges and how are they best approached?

## Slide 22: Rescue
Riley Rover (Victoria only)
Push victim completely out of chemical spill
Primary Rescue
Push victim completely out of chemical spill
Exit chemical spill and recapture line (new in 2021)
Secondary Rescue
Control and release victim in an upright position outside the swamp
Exit chemical spill and recapture line
Open Rescue
Lift victim onto rescue platform in upright position
Exit chemical spill and recapture line

## Slide 23: Entering chemical spill and detecting the victim
How can the robot detect chemical spill tile?
Highly reflective tape at entrance
How can the robot detect the victim?
For Riley Rover, it doesn’t need to but more efficient if it does
How can the robot control the victim?
What level of control is needed for each division?
How can the robot exit the spill and regain the line?
Not required for Riley Rover

## Slide 24: Think through problem – Detecting the spill tile
Detecting chemical spill
Does the reflected value for the foil tape differ from white?
Does the tape have a colour value?
Are measured values for reflected light and colour consistent?
With Spike Prime it is possible to measure the raw red, green and blue values individually. Can this help distinguish the silver foil from white?

## Slide 25: Think through problem – Finding the victim
Finding victim
Ultrasonic sensor measures distance from object
Where is the best place to position the robot to begin checking?
What is the maximum distance the victim could be from the robot?
What happens if the sensor is too close to the victim?
Is the ultrasonic sensor able to detect curved surfaces as easily as flat surfaces?
What if alignment is not perfect?
Transmitter
Receiver

## Slide 26: Thinking through problem – Rescuing the victim
Controlling the victim (secondary)
Grabber mechanism
  Positive: Can get away with not being perfectly lined up since grabber will gather victim in
  Negative: Can be bulky and add to length of robot resulting in course navigation problems
Cage mechanism
  Positive: Much more compact
  Negative: Need precise alignment
Rescuing the victim
Push/drag rescue capsule to white and release
What happens if the robot has missed or lost control of the rescue capsule?

## Slide 27: Think through problem – Finding exit and regaining the line
Finding exit (3 options – are there others?)
Use single light sensor line follower algorithm to follow edge of green until reflective tape is reached
  Where would you position the robot relative to the edge?
Random or systematic “walk” until reflective tape is detected
Record and retrace steps

## Slide 28: Additional challenges
Detecting intersections
Navigating around water tower

## Slide 29: Detecting green at intersections
Robots should turn in the direction of the green marker

## Slide 30: Detecting green at intersections
NOTE: The green on Rescue challenge mats used in the Victorian competitions are detected as green by Lego EV3 colour sensors. This is not necessarily the case for all Rescue mats and may not be true if sensors change. There is nothing in the national rules that specifies the shade of green.
Thinking through the problem:
Does the robot turn correctly using a basic line following program? Always? Most of the time? Rarely? Never?
Do the colour sensors detect the “green” as “green”?
  Spike Prime colour sensors seem to be more reliable than EV3 sensors
What are the reflected light values when over the green squares? Are they unique individually? As a sum? As a difference? Can you use any of this to reliably detect green?

## Slide 31: Navigating around water tower
What should be used to detect the water tower (Ultrasonic? Touch?)?
It is relatively easy to pre-program a route around tower, but …
  What happens if robot isn’t perfectly aligned with water tower?
  How does the robot know when it has found the line again?
Must recapture the line on the same tile to get points

## Slide 32: Troubleshooting
Check that:
Port settings in program match ports on robot
Movement motors have been defined correctly
Actual reflected light/colour readings correspond to values set in program
Motor power values are reversed in program if motors are in reverse orientation
All conditional statements are set correctly
Sounds/displays aren’t affecting program flow
And a few tips
Program in small increments
Use the brick displays or sounds to help identify if a particular part of the program is being
Use My Blocks to help organise more complex programs
Save programs with significant changes as a new version, so stable older versions are not lost
On competition days make sure that programs loaded on the brick are functional programs (don’t leave rubbish programs on the brick that could be run by accident)
Make sure that battery is charged